## Slide 1: Unit – 6
Frequency Management and Channel Assignment

## Slide 2: Frequency Management
Frequency management
  Designating set-up channels and voice channels (done by the FCC),
  Numbering the channels
  (done by the FCC), and
  Grouping the voice channels into subsets
  (done by each system according to its preference).

## Slide 3: Channel assignment
    Means the allocation of specific channels to cell sites and mobile units.
A fixed channel set – Cellsite- long-term basis
During a call- Mobile unit - short-term basis (handled by MTSO).

## Slide 4: Channel Assignment
Ideally channel assignment should be based on causing the least interference in the system.

## Slide 5: Numbering the Channels
The total number of channels (January 1988) is 832.
But most mobile units and systems are still operating on 666 channels.
A channel consists of two frequency channel bandwidths,
  one in the low band
  one in the high band

## Slide 6: Numbering the Channels
Two frequencies in channel 1 are
  825.030 MHz (mobile transmit) and
  870.030 MHz (cell-site transmit)
The two frequencies in channel 666 are
  844.98 MHz (mobile transmit) and
  889.98 MHz (cell-site transmit)

## Slide 7: Numbering the Channels
The 666 channels are divided into two groups:
  block A system
  block B system

## Slide 8: Frequency-management chart.

## Slide 9: Numbering the Channels
Each block has 333 channels
The 42 set-up channels are assigned as follows.
  Channels 313 - 333 block A
  Channels 334 - 354 block B
The voice channels are assigned as follows.
  Channels 1 - 312 (312 voice channels) block A
  Channels 355 - 666 (312 voice channels) block B

## Slide 10: Numbering the Channels- additional spectrum allocation
New additional spectrum allocation - 10 MHz -additional 166 channels are assigned
a 1 MHz is assigned below 825 MHz (or 870 MHz)
additional channels will be numbered up to 849 MHz (or 894 MHz) and will then circle back
The last channel number is 1023 (=210)
There are no channels between channels 799 and 991.

## Slide 11: New additional spectrum allocation

## Slide 12: Full Spectrum Frequency Management

## Slide 13: Full Spectrum Frequency Management

## Slide 14: Grouping into Subsets
Voice channels for each system is 312
We can group these into any number of subsets
21 set-up channels for each system
it is logical to group the 312 channels into 21 subsets
Each subset then consists of 16 channels
In each set, the closest adjacent channel is 21 channels away

## Slide 15: Grouping into Subsets
The 16 channels in each subset - connected to a channel combiner
Wide separation between adjacent channels -requirement of minimum isolation
Each 16-channel subset is idealized for each 16-channel combiner

## Slide 16: Grouping into Subsets
In a seven-cell pattern system each cell contains three subsets,
iA + iB + iC
where i is an integer from 1 to 7
The total number of voice channels in a cell is about 45
The minimum separation between three subsets is 7 channels (21/3)

## Slide 17: Grouping into Subsets
If six subsets are equipped in an omnicell site,
Minimum separation between two adjacent channels can be only three (21/6 > 3) physical channel bandwidths
For Example

## Slide 18: Techniques for increasing frequency spectrum
Increasing the number of radio channels using narrow banding, spread spectrum, or time division
Improving spatial frequency-spectrum reuse
Frequency management and channel assignment
Reducing the load of invalid calls
  Voice storage service for No-Answer calls
  Call forwarding
  Call waiting for Busy-Call situations
  Queuing

## Slide 19: Set-up Channels
Set-up channels, also called control channels,
Channels designated to set up calls
A system can be operated without set-up channels
Set-up channels can be classified by usage into two types
  access channels
  paging channels

## Slide 20: Access channels - Operational functions
Power of a forward set-up channel [or forward control channel (FOCC)]
The set-up channel received level (Threshold)-RECC
Change power at the mobile unit(Messages)
  Mobile station control message
  System parameter overhead message
  Control-filler message
Direct call - retry

## Slide 21: Mobile station control message
DCC – Digital Color Code
  A Digital Signal transmitted by an FOCC to detect capture of an interfering mobile station
  Mobile station uses DCC to identify the land station
MIN
VMAX
SCC

## Slide 22: SCC – SAT Color Code

## Slide 23: System parameter overhead message
DCC
SID - A digital identification uniquely associated with a cellular system(15-bit)
CMAX
CPA - Combined paging/access
  CPA = 1 Paging &access channel are the same
  CPA = 0 Paging &access channel are not the same

## Slide 24: Control-filler message
CMAC - a control mobile attenuation code
the mobile station has to adjust its transmitter power level before accessing a system on a RECC

## Slide 25: Paging Channels
The assigned forward set-up channel (FOCC) of each cell site is used to page the mobile unit with the same mobile station control message

## Slide 26: Selecting a voice channel
For mobile-originating calls
For paging calls

## Slide 27: Channel Assignment to the Cell Sites-Fixed Channel Assignment
Set-up channels & Voice channels
long-term basis

## Slide 28: Fixed Channel Assignment
Setup-channels
  21 channels
  N = 4, 7, 12 cell reuse patterns
  Omni-directional antennas
  One channel per cell
  Unused set-up channels
  Avoid interference between block A and B

## Slide 29: Fixed Channel Assignment
Voice Channels
  21 subsets
  Min. cochannel & Adjacent channel interference
3 SAT Tones

## Slide 30: Channel Assignment to Travelling Mobile Units
Underlay-overlay
Frequency Assignment
Tilted Antenna

## Slide 31: Channel Assignment to Travelling Mobile Units
Underlaid-overlaid cell arrangements
(a) Undelay-overlay in omnicell (b) underlay-overlay in sectorized cells
(c) two-level handoff scheme

## Slide 32: Underlay-overlay arrangement

## Slide 33: Fixed Channel Assignment
Adjacent-Channel Assignment
Channel Sharing and Borrowing
Sectorization

## Slide 34: Adjacent-Channel Assignment
Adjacent channel assignment.
(a) Omnidirectional-antenna cells (b) directional-antenna cells

## Slide 35: Channel Sharing and Borrowing
Channel Sharing
Algorithm

## Slide 36: Sectorization
The 120o sector cell for both transmitting and receiving
The 60o sector sell for both transmitting and receiving
120o or 60o sector cell for receiving sectorization only , and transmitting antenna is omni-directional

## Slide 37: Non-Fixed Channel Assignment algorithms
Dynamic Channel Assignment
Hybrid channel Assignment
Borrowing channel Assignment
Forcible-borrowing channel Assignment

## Slide 38: Simulation process and results
Cellular system.
Vehicle and radio-channel distribution in the busy rush hour

## Slide 39: Simulation process and results
Average Blocking
Handoff Blocking